## Slide 1
“MANHOLE DETECTION AND MONITORING”
DEPARTMENT OF ELECTRONICS AND COMMUNICATION ENGINEERING
REAL TIME PROJECT PRESENTATION ON
TEAM MEMBERS:
T. Sai Chandana – 22D41A04B4
V. Sneha.
V. Mukthavali
– 23D45A0412
– 23D45A0413
SRI INDU COLLEGE OF ENGINEERING & TECHNOLOGY
(An Autonomous Institution under UGC, New Delhi)
Recognized under 2(f) and 12(B) of UGC Act. 1956 Sheriguda village, Ibrahimpatnam, RR District – 501 510, T.S,INDIA

## Slide 2: 01
04
02
05
03
06
CONTENTS
Introduction
Components required
Working
Block diagram
Future Enhancement
07
08
Benefits
Conclusion
Applications

## Slide 3: INTRODUCTION
The aim of the manhole detection and monitoring project is to enhance the safety, efficiency, and reliability of urban infrastructure by providing real-time monitoring of manhole conditions.
This system seeks to prevent accidents, ensure environmental safety, and facilitate proactive maintenance through the use of various sensors.
Manhole monitoring is essential for protecting maintenance workers from hazardous conditions such as toxic gases and flooding, as well as safeguarding the public from accidents involving unauthorized access.

## Slide 4: COMPONENTS
IR Tilt Sensor:
Specifications:
Operating Voltage: 3.3V - 5V Output: Digital
Detection Angle: Typically, up to 90 degrees tilt
HC-SR04 Ultrasonic Sensor:
Specifications:
Operating Voltage: 5V
Operating Current: 15mA Measuring Range: 2cm - 400cm Resolution: 0.3cm
Ultrasonic Frequency: 40kHz
PIR Motion Sensor:
Specifications:
Operating Voltage: 5V
Detection Range: Up to 7 meters Detection Angle: 110 degrees
Output: Digital (High when motion detected)

## Slide 5
MQ2 Gas Sensor:
Specifications:
Operating Voltage: 5V
Detection Range: 300 - 10000 ppm Preheat Time: 20 seconds
Sensitivity: Adjustable via potentiometer Analog Output: Varies with gas concentration
GPS Module:
Specifications:
Operating Voltage: 3.3V - 5V
Communication: UART (Serial) Baud Rate: 9600 (common) Position Accuracy: 2.5 meters CEP
ESP8266 NodeMCU:
Specifications: Operating Voltage: 3.3V Digital I/O Pins: 17
Analog Input: 1 (max input 3.3V)
Flash Memory: 4MB Wi-Fi: 802.11 b/g/n

## Slide 6: LCD Display:
Specifications:
Operating Voltage: 5V
Interface: I2C
Address: Typically 0x27 or 0x3F Characters: 16 per line, 2 lines
Power Supply: A power supply is a crucial component in electronic systems, providing the necessary electrical power for the operation of devices and circuits. It converts electrical energy from a source to the correct voltage, current, and frequency required by the load.
Bread board: It is used make the connections required in a circuit.

## Slide 7: BLOCK DIAGRAM
PIN CONFIGURATION

## Slide 8: WORKING
This project employs an ESP8266 microcontroller to monitor environmental conditions in a manhole using various sensors, with data displayed on an LCD and uploaded to ThingSpeak for remote monitoring.
It includes a PIR sensor to detect motion, an IR sensor to sense obstacles, a gas sensor to measure hazardous gases, an ultrasonic sensor to determine distance, and a GPS module to provide location coordinates.
Initially, the ESP8266 sets up the LCD, sensors, and WiFi connection. It collects data from each sensor: motion detection from the PIR sensor, obstacle presence from the IR sensor, gas concentration levels, and distance measurements.
If any sensor detects hazardous conditions—such as motion, obstacles, high gas levels, or close distances—an alert state is triggered, and an alert function is called.
This data, including the alert status, is then uploaded to ThingSpeak for continuous remote monitoring, with the system repeating these steps every second to ensure real-time surveillance.
This comprehensive setup helps promptly detect and report dangerous conditions within the manhole, thereby enhancing safety and enabling timely interventions.

## Slide 11: OUTPUTS

## Slide 12: BENEFITS
The benefits of the manhole monitoring
system include:
Enhanced Safety
Environmental Protection
Efficient Maintenance
Remote Monitoring and Data Analysis
Operational Efficiency
Cost Savings
Preventing Accidents
Crime Prevention
Early Detection of Issues
Flood Prevention

## Slide 13: APPLICATIONS
Urban Infrastructure Management
Public Safety
Flood Prevention
Environmental Protection
Construction And Development
Smart City Initiatives

## Slide 14: FUTURE ENHANCEMENT
GSM Module: Incorporate GSM modules to enable data transmission and alerts via mobile networks, ensuring connectivity even in areas without Wi-Fi coverage.
LoRaWAN: Utilize LoRaWAN technology for long-range, low-power communication, ideal for monitoring manholes spread over large areas.
Solar Power: Utilize solar panels to power the monitoring system, making it more sustainable and reducing the need for frequent battery replacements.
Data Management Challenges
Maintenance and Upkeep

## Slide 15: CONCLUSION
Manhole detection and monitoring systems provide significant advantages in terms of safety, efficiency, cost savings, and environmental protection.
By leveraging advanced technologies such as sensors, connectivity, and data analytics, these systems enable proactive and effective management of urban infrastructure, contributing to the overall well-being and safety of the community.
Manhole detection and monitoring systems are versatile
and beneficial in a wide range of applications.

## Slide 16: THANK YOU!